Working with the APDS-9960
1. Perform sudo git clone https://github.com/GeekyTim/PiHue
2. Perform sudo git clone https://github.com/liske/python-apds9960.git
3. Connect APDS-9960 leads to Raspberry Pi, 3.3V, SDA, SCL, Gnd.
4. Activate Raspberry Pi I2C comm system via Preferences→Raspberry Pi Configuration→Interfaces→I2C.
  1. Verify connection by running terminal command ‘i2cdetect -y 1’. This should return a ‘39’ somewhere in the block of code. That means that the device is detected.
5. Built Python program with Thonny. Ambient and RGB sensors returned values.
  1. Installed Pinta paint program to create colors for testing the sensor
    1. sudo apt-get install pinta
  2. Test results:
    1. Applied 3 tests, RGB color pour value 255 for each RGB
    2. No R, G, or B value fell to 0 for any of the color selections, though the sensor did appear to correctly show color dominance of the test color.
      Scrn Raw Percent
      R 255 173 71.2
      G 0 25 10.4
      B 0 46 18.5

      R 0 70 15.5
      G 255 240 53.3
      B 0 138 31.1

      R 0 11 5.8
      G 0 50 25.0
      B 255 138 69.2
    3. Interpretation
       The failure to sense the “pure 255” samples from the screen may be due to the physical characteristics of the sensing diodes for RGB. R has greatest sensitivity to ~605nm wavelength, but according to the graphic in the APDS-9960 manual, page 7, it is sensitive on the range of 550nm to 675nm. G is sensed in the range of 450nm to 600nm, which crosses into the red sensing range.
       This may cause difficulty reproducing a color.
6. Begin testing program in terminal.
  1. Found that terminal is running Python 2.5. Thonny is using Python 3.5.
    1. Install Python 3.5: sudo apt-get install python3.5
    2. Investiage file/folder names. ls /usr/bin/python*
    3. Added Python alternatives.
       sudo update-alternatives --install /usr/bin/python python /usr/bin/python2.7 1
       sudo update-alternatives --install /usr/bin/python python /usr/bin/python3.5 2
    4. Checked for alternatives.
       update-alternatives --list python
    5. Check default Python version.
       Python -V
      1. Confirmed now using Python 3.5.3.
  2. Run program in terminal.
     cd APDS9960_Test/
     python APDS9960_Test.py
7. Controlling the Hue
  1. Install requirements
    1. Ran from terminal: pip3 install phue
    2. Modified PiHueLightList.py to meet needs.
      1. Pressed the connect button on the Hue Bridge.
      2. Ran code – Hue bridge connection successful
      3. Modified code to omit connection data initialization
      4. Tested successfully
8. Create combined system
  1. Created folder NatHue. Copied requirements. Merged programs.
  2. Tested successfully
9. Make program run on boot.
  1. Created a script to run the program, NatHue.sh
  2. Running script via rc.local in etc folder.
10. Install software to run the display screen.
  1. Installed Python imaging library and smbus library using this command:
     sudo apt-get install python-smbus
     sudo apt-get install libjpeg8-dev
     pip install Pillow
  2. Install SSD1306 library
     git clone https://github.com/adafruit/Adafruit_Python_SSD1306.git
  3. Navigate to directory and install for Python 3
     cd adafruit_Python_SSD1306
     sudo python3 setup.py install
  4. Test screen
     cd examples
     python stats.py